## Slide 1: CS310 Operating Systems Lecture 40 : Hard Disk Storage
Ravi Mittal
IIT Goa

## Slide 2: References
CS162, Operating Systems and Systems Programming, University of California, Berkeley
Various websites on the Internet

## Slide 3: Reading
CS162, Operating Systems and Systems Programming, University of California, Berkeley
Book: Operating System Concepts, 10th Edition, by Silberschatz, Galvin, and Gagne

## Slide 4: Lecture Contents
Persistent Storage Technologies
Hard Disk Drives
Solid State Drive (SDD)

## Slide 5: Where are we?
Compiler
Process 2
Running
Program 2
System Libs
Processor
Memory
PgTbl
& TLB
Storage
Networks
Hardware
I/O Ctrlr
ISA
Operating System
Process 1
Threads
OS Mem
Address Spaces
Files
Sockets
Threads
Address Spaces
Files
Sockets
Running
Program 1
System Libs
Kubiatowicz CS162 © UCB Spring 2021

## Slide 6: Persistent Storage Technologies

## Slide 7: Persistent Storage for File System
I/O API and
syscalls
Variable-Size Buffer
File System
Block
Logical Index, Typically 4 KB
Hardware Devices
Memory Address
HDD
Sector(s)
Physical Index,
512B or 4KB
SSD
Flash Trans. Layer
Phys. Block
Phys Index., 4KB
Sector(s)
Sector(s)
Erasure Page
CS162 © UCB Fa19

## Slide 8: Storage Technologies
Magnetic Disks
Store on magnetic medium
Electromechanical access
Nonvolatile (Flash) Memory
Store as persistent charge
Implemented with 3-D structure
  100+ levels of cells
  3 bits data per cell
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 9: RAM vs Hard Disk vs SSD - 2018
In SSD Each cell has limited program/erase lifetime (thousands, for modern devices) – Cells become slowly less reliable

## Slide 10: Popular Storage Devices
Magnetic Disks
Rarely becomes corrupted
Traditionally: large capacity at low cost
Block level random access
Slow performance for random access
Better performance for sequential access
Flash Memory
Rarely becomes corrupted
Increasingly larger and cheaper
Block level random access
Good performance for reads, worse for random writes
Have to erase data in large blocks
Challenge: Wear Levelling

## Slide 11: Emergence of SSDs

## Slide 13: The Emergence of SSDs
Faster
Lower power
No moving parts
But HDDs have their place
  Cheapest online storage per byte
  Application: Archival storage
CS162 Univ of California Berkeley

## Slide 14: Hard Disk Drives (HDD)

## Slide 15: Hard Disk Drivers (HDDs)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)
CS162 Univ of California Berkeley

## Slide 16: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)
CS162 Univ of California Berkeley

## Slide 17: Disk platter – top view
Typically sector = 512 bytes
Minimum reading on disk: 1 sector
  Can’t read individual byte or word

## Slide 18: The Amazing Magnetic Disk
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk

## Slide 19: Shingled Magnetic Recording (SMR)
Shingled magnetic recording is a magnetic storage data recording technology used in hard disk drives to increase storage density and overall per-drive storage capacity
Overlapping tracks yields greater density, capacity
Restrictions on writing, complex DSP for reading

## Slide 20: Review: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surfaces
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track –Average of 5-10 ms
  Rotational latency: wait for desired sector to rotate under r/w head
    4-8 ms (3600-7200 rpm), 2-4 ms (15000ms)
  Transfer time: Time to actually read sectors
    50-100 MB/sec
Sector
Track
Cylinder
Head
Platter
CS162 Univ of California Berkeley

## Slide 21: Bigger Picture
Latency = Queue Time + Controller Time + Seek Time + Rotational Latency + Transfer Time
To Achieve Best Bandwidth: Large Transfers of Physically Adjacent Sectors from one track
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
CS162 Univ of California Berkeley

## Slide 22: Disk Performance Example – Self reading
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000 (ms/min) / 7200(rev/min) ~= 8ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec  0.082 ms per block
Read block from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track:
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 23: HDD Controller

## Slide 24: HDD Controllers
Old Days: Device driver would address block of data by cylinder number, head (platter) number, and sector number
Now: Hard drive is just an array of sectors
  Sector number mapped internally to physical location
  Numerically close sectors are probably physically close
Lots of other intelligent features
  Error Correcting Codes
  Sector Sparing
  Slip Sparing
  Track Skewing
CS162 Univ of California Berkeley

## Slide 25: Intelligence in the Controller
Error Correcting Codes
  Disk encodes each sector with additional error correcting code data – allowing it to fix imperfectly read or written data
Sector sparing
  Disks are made with tracks and sectors as thin and small as possible
  If there are imperfections in a sector, then the sector can not be used for reliably store data
  Manufacturers include spare sectors distributed across each surface
  Disk firmware or formatting can remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
  Helps in retaining good sequential performance by remapping all sectors from the bad sector to the next spare

## Slide 26: Intelligence in the Controller
Track Skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential operations
  Logical sector zero on each track is staggered from sector zero on the previous track
    By an amount corresponding to time it takes the disk to move the head from one track to another

## Slide 27: Typical Numbers for Magnetic Disk (self reading)
Parameter | Info/Range
Space/Density | Space: 14TB (Seagate), 8 platters, in 3½ inch form factor! Areal Density: ≥ 1 Terabit/square inch! (PMR, Helium, …)
Average Seek Time | Typically 4-6 milliseconds
Average Rotational Latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 4-8 milliseconds
Controller Time | Depends on controller hardware
Transfer Time | Typically 50 to 250 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or faster), now slowing down

## Slide 28: Example of Current HDDs (Self reading)
Seagate Exos X14 (2018)
  14 TB hard disk
    8 platters, 16 heads
    Helium filled: reduce friction and power
  4.16ms average seek time
  4096 byte physical sectors
  7200 RPMs
  6 Gbps SATA /12Gbps SAS interface
    261MB/s MAX transfer rate
    Cache size: 256MB
  Price: $615 (< $0.05/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB, 340,000x more expensive !!)
CS162 Univ of California Berkeley

## Slide 29: Lecture Summary
Hard Disk Drives – had magical run
Tremendous improvement in HDD technology
  Smaller sizes
  More information
  Less power
  Low cost
  Improved Performance
  Higher reliability
  A lot of intelligence
SSD are now becoming main stream